## Slide 1: Demonstrating ACI Network Programmability and Orchestration
Cisco ACI Configuration and Orchestration

## Slide 2: Business Need for Network Programmability
Networks are growing in the data center.
  There are new demands to accommodate new and more applications.
  More devices need to be managed.
Uptime is critical to the business, as is shorter deployment time.
High value engineers are being asked to focus on strategic tasks and shift away from maintenance.
Manual, incremental, switch-by-switch configuration introduces risk and time delay.
Open programmability provides a skill that can be used across many platforms. Networking needs to transition to this type of programmability.

## Slide 3: ACI Programmability
Built-in programmability in both software and hardware
Entire infrastructure can be programmed as a single fabric
Declarative model enforces desired state

## Slide 4: ACI Programmability (Cont.)

## Slide 5: ACI Open APIs and Ecosystem
REST API chosen for northbound layer.
APIC supports a rich ecosystem built around open northbound and southbound APIs.

## Slide 6: API Protocols
A web service API allows devices to communicate using HTTP calls.
What is the best protocol for an API and why?
  SOAP is overly complex.
  REST fits well with HTTP.
  REST aligns well with scalability, caching, and distribution in web applications.
  JSON is the most widely adopted message format.

## Slide 7: How Is REST Used?
Resources accessed can be what you want.
  Usually data, tables, methods
How you return the resources is your choice.
Generally data is returned as XML or JSON, but could be a picture.
  Example: Read data in a database table
  Server: Myserver
  Database: MyDB
  Table: Table1
  http://Myserver/MyDB/Table1

## Slide 8: What Is XML?
XML is much like HTML.
XML stores information, HTML displays information.
XML does not do anything on its own. XML requires software to send, receive, display, and act on the information in the XML store.
The XML language has no predefined tags or document structure.
XML data is stored in plaintext format providing a software- and hardware-independent way of storing data for application sharing.
<?xml version="1.0" encoding="ISO-8859-1"?> <note> < to>James</to> < from>Debbie</from> < heading>Reminder</heading> < body>Don't forget my birthday!</body> < /note>

## Slide 9: What Is JSON?
The JSON format is specified in RFC 4627.
JSON is a lightweight data format used in web services for transmitting data.
JSON uses arrays and has no reserved words.
{ "firstName": "John", "lastName": "Smith", "address": { "streetAddress": "21 2nd Street", "city": "New York", "state": "NY", "postalCode": 10021 }, "phoneNumbers": [ "212 555-1234", "646 555-4567" ] }

## Slide 10: What Is JSON? (Cont.)
{ "employees": [ { "firstName":"John" , "lastName":"Doe" }, { "firstName":"Anna" , "lastName":"Smith" }, { "firstName":"Peter" , "lastName":"Jones" } ] }
The employees object is an array of three employee records (objects).

## Slide 11: Evaluating XML and JSON
JSON is simpler than XML and more compact.
  XML is more verbose than JSON, so JSON is faster for humans to write.
  XML parsing is hard because of its complexity.
JSON is a better fit for object-oriented systems than XML.
JSON is not as extensible as XML.
JSON is preferred by many for simple data exchange.
With JSON, there is less syntax and no semantics.
Schemas are not needed.

## Slide 12: Evaluating XML and JSON (Cont.)
XML <car> <company>Volkswagen</company> <name>Vento</name> <price>800000</price> </car>
JSON { "company": Volkswagen, "name": "Vento", "price": 800000 }

## Slide 13: Northbound: REST API, Python, Puppet, Chef, OpenStack
Description
  Based on open ACI object model
  Foundation for integration with open-source and third-party tools
  JSON or XML over HTTP
OSS software and standards
  Published object model and documentation
  Simulator environment available
  Open-source Python SDK
  Open-source Neutron plug-in (OpenStack)
  Open-source cookbooks for DevOps

## Slide 14: ACI Fabric-Attached Device API—OpFlex
Open an API between a controller and a set of network devices designed to natively support ACI policy.
This feature is supported over TCP, SSL, and HTTP.
The logical policy model is pushed directly from the controller (policy authority) to a device (policy element) that renders the model in software and hardware.
Policy elements can be leaf switches in a network fabric, hypervisor switches, or Layer 4 to Layer 7 devices.
An open-source C-based OpFlex agent will be released.

## Slide 15: Southbound: Layer 4 to Layer 7 Scripting API
Description
  Supports service insertion and chaining of devices
  Device specification: Object model for device
  Device script: Integration script using existing APIs of device
OSS software and standards
  Device packages for most major vendors will be released as open source.

## Slide 16: Cisco DevNet—New Developer Program from Cisco
All of the developer resources that you need are centralized in one location:
  Comprehensive API index
  Forums
  Developer sandbox
  FAQs
  Access to support, and more
The interactive new portal makes finding information and support faster and easier.

## Slide 17: Community Code Development
ACI and Cisco NX-OS code examples and libraries
Open-source and community-developed tools by partners and third-party developers

## Slide 18: What Is REST?
REST is an architectural style in which clients initiate requests to servers. Servers process requests and return appropriate responses.
  Get: Get list of tasks or task by ID.
  Post: Create a new task.
  Put: Add to existing task by ID.
  Delete: Delete an existing task by ID.
The World Wide Web represents the largest implementation of a system conforming to the REST architectural style.
A RESTful web API (also called a RESTful web service) is a web API implemented using HTTP and REST principles.
REST is an HTTP-based protocol.
The client, typically a web browser, needs to construct HTTP requests and parse XML or JSON responses.

## Slide 19: REST APIs
A REST API is a fancy name for a web-based API that expects some data as input (typically XML) posted to a well-known URL.
The data is usually sent via an HTTP POST (sometimes GET, sometimes DELETE) as plain XML, JSON, or text with no particular envelope or wrappers.
Processing happens server-side and data is sent back, typically as XML, JSON, or plaintext.
Requests are usually fire-and-forget (or atomic). You make a Create, Request, Update, Delete (CRUD) operation corresponding to the four REST methods.
REST APIs are common and widely used (VMware, AWS, Google, Microsoft, Cisco UCS, and so on).

## Slide 20: Configuration and the RESTful API
The same API is used by all interfaces with the APIC.
  CLI, GUI, and SDK all use the REST interface.
Configuration is written via the API.
Information is read via the API:
  Statistics
  Faults
  Events
  Configuration

## Slide 21: What Is RPC Used For?
RPC gives developers a mechanism for defining interfaces that can be called over a network.
XML-RPC uses HTTP as the transport and XML as the encoding.
XML-RPC makes no assumption about the client that is using the protocol.
REST, being an HTTP-based protocol, works best when the client is a browser.
Web services should provide an XML-based interface like XML-RPC with a RESTful interface on top for browser-based clients.

## Slide 22: ACI APIC Object-Based Tree
Everything is an object and objects are hierarchically organized.
Packages identify the functional area. For example, fv = fabric virtualization, vz = virtual zones, fabric = physical fabric, and so on.
Class identifies object type.
  Card, port, path, EPG, and so on
  Access port is a subclass of port
  A leaf node is a subclass of fabric node
Sets of attributes include identity, state, description, references, and lifecycle.
The dMIT contains comprehensive system information:
  Discovered components
  System configuration
  Operational status including statistics and faults

## Slide 23: APIC REST API Operations
Everything is represented as an object and every object can be manipulated via REST.
  REST operations (methods): POST, GET, DELETE
  Support for JSON and XML
API calls are fully transactional across independent fabric components.
Consistent naming is mapped to URLs.

## Slide 24: APIC REST API Operations (Cont.)
Comprehensive access is provided through API.
The APIC Simulator simulates a leaf and spine fabric.

## Slide 25: APIC REST API Message Format
Format: http://host[:port]/api/{mo|class}/{dn|className}.{json|xml}[?options]
  /api/: Specifies that the message is directed to the API.
  mo|class: Specifies if the target of the operation is a managed object or an object class.
  dn: Specifies the unique distinguished name of the targeted managed object.
  className: Specifies the name of the targeted class.
  json|xml: Specifies if the encoding format of the command or response HTML body is JSON or XML.
Example: Find all 10G ports on the fabric.
  http://apic/api/l1PhysIf.xml?query-target-filter=eq(l1PhysIf.speed, "10G")

## Slide 26: dMIT Queries

## Slide 27: Managed Object Properties
The object itself is presented to the user through the RESTful API as a single entity compiled at runtime.
Three processes are writing to property chunks of the object:
  DME
  Port Manager
  STP

## Slide 28: REST API Example—Authenticate
Authenticate a user for API operation
POST: http://apic1/api/aaaLogin.xml
Body (XML):<aaaUser name="georgewa" pwd="paSSword1" />

## Slide 29: REST API Example—Authenticate (Cont.)

## Slide 30: Creating a Tenant

## Slide 31: Creating an Application Network Profile

## Slide 32: Object Browser: Visore
APIC has a built-in object browser to navigate the object tree and inspect the state of objects.
Point the web browser to Visore: http://apic/visore.html.
Search for a particular object or dn (fvTenant, topSystem, topology/pod-1/node-101).

## Slide 33: Object Browser: Visore (Cont.)

## Slide 34: Cisco ACI SDK
The Cisco ACI Python SDK is named Cobra.
Python implementation of the API.
Provides native bindings for all the REST functions.
Cobra provides methods that match the REST methods used by the GUI.
Policy created in the GUI can be used as a programming template.

## Slide 35: Cisco ACI Cobra SDK Installation
Possible to use standard Python distribution utilities
Cobra comes in two installable .egg files:
  acicobra: the SDK
  acimodel: includes the Python packages that model the Cisco ACI Management Information Tree
.egg files can be installed using easy_install

## Slide 36: Connecting and Authenticating to APIC
Example of connecting and authenticating to APIC:
apicUrl = 'https://192.168.10.80' loginSession = LoginSession(apicUrl, 'admin', 'mypassword') moDir = MoDirectory(loginSession) moDir.login() # Use the connected moDir queries and configuration .... moDir.logout()

## Slide 37: Example – Creating a Tenant
Example of connecting and authenticating to APIC:
# Import the config request from cobra.mit.request import ConfigRequest configReq = ConfigRequest() # Import the tenant class from the model from cobra.model.fv import Tenant # Get the top level policy universe directory uniMo = moDir.lookupByDn('uni') # Create the tenant object fvTenantMo = Tenant(uniMo, 'ExampleCorp')

## Slide 38: Cisco APIC REST to Python Adapter

## Slide 39: ACI GUI Is API Driven
API Inspector allows a window into the data structures:
  Mirrors API calls to controller
  Useful for programmers
  Opens up APIC to application integration

## Slide 40: ACI GUI Is API Driven (Cont.)

## Slide 41: Capturing API Calls

## Slide 42: Summary
Open programmability provides a single skill that can be extended across many platforms for many tasks and can help achieve the business needs of more dynamic and accurate deployments for networking infrastructure.
JSON and XML are human readable formats and are language independent. Both formats have support for creation, reading, and decoding in real-world situations.
All configuration is performed in the ACI fabric through the RESTful API, regardless of the interface used for managing the fabric through the API, including the native GUI and CLI of the APIC.
The APIC API Inspector is accessible through the menu bar of the Cisco APIC and provides a mirror of all the API calls performed by the GUI on the fabric controller.
OpFlex is a new extensible policy resolution protocol designed for declarative control of any data center infrastructure from the Cisco APIC. Using the declarative model, the application policy is now completely abstracted from the network.

## Slide 43: Summary (Cont.)
Cisco, together with other vendors like IBM, has been working on a project to extend the Neutron plug-in capability to map the OpenStack API to a group policy structure. For Cisco, this ability would enable integration with the application network policy of ACI.
Cisco has taken the Neutron Group Policy Model abstraction seen in OpenStack to the OpenDaylight project to allow the group-based policy model to be rendered by the OpenDaylight controller. This feature will be available in the future, but no date is specified yet for availability.

## Slide 44: Closing Logo Slide

## Slide 45
Object Store Browser- Visore
Notes: Once the location is obtained, we can use this information to use the “Object Store Browser” to learn the schema.

## Slide 46
Distinguished Names and Classes
The Class name
The DN name
Notes: The distinguished name enables you to unambiguously identify a specific target object. The distinguished name consists of a series of relative names:
dn = {rn}/{rn}/{rn}/{rn}...
In this example, the DN provides a fully qualified path for the Atlanta Tenant
object. The DN specifies the exact managed object on which the API call is operating.
< dn =”uni/” />

## Slide 47
Distinguished Names and Classes
Notes: The distinguished name enables you to unambiguously identify a specific target object. The distinguished name consists of a series of relative names:
dn = {rn}/{rn}/{rn}/{rn}...
In this example, the DN provides a fully qualified path for the Atlanta Tenant
object. The DN specifies the exact managed object on which the API call is operating.
< dn =”uni/” />

## Slide 48
Mapping Documents to the Schema
Notes: The distinguished name enables you to unambiguously identify a specific target object. The distinguished name consists of a series of relative names:
dn = {rn}/{rn}/{rn}/{rn}...
In this example, the DN provides a fully qualified path for the Atlanta Tenant
object. The DN specifies the exact managed object on which the API call is operating.
< dn =”uni/” />

## Slide 49
Mapping Documents to the Schema
Notes: The distinguished name enables you to unambiguously identify a specific target object. The distinguished name consists of a series of relative names:
dn = {rn}/{rn}/{rn}/{rn}...
In this example, the DN provides a fully qualified path for the Atlanta Tenant
object. The DN specifies the exact managed object on which the API call is operating.
< dn =”uni/” />

## Slide 50
Mapping Documents to the Schema
Notes: The distinguished name enables you to unambiguously identify a specific target object. The distinguished name consists of a series of relative names:
dn = {rn}/{rn}/{rn}/{rn}...
In this example, the DN provides a fully qualified path for the Atlanta Tenant
object. The DN specifies the exact managed object on which the API call is operating.
< dn =”uni/” />

## Slide 51
Mapping Documents to the Schema
Notes: The distinguished name enables you to unambiguously identify a specific target object. The distinguished name consists of a series of relative names:
dn = {rn}/{rn}/{rn}/{rn}...
In this example, the DN provides a fully qualified path for the Atlanta Tenant
object. The DN specifies the exact managed object on which the API call is operating.
< dn =”uni/” />

## Slide 52
Distinguished Names and Classes
Notes: The distinguished name enables you to unambiguously identify a specific target object. The distinguished name consists of a series of relative names:
dn = {rn}/{rn}/{rn}/{rn}...
In this example, the DN provides a fully qualified path for the Atlanta Tenant
object. The DN specifies the exact managed object on which the API call is operating.
< dn =”uni/” />

## Slide 53
Mapping Documents to the Schema
Notes: The distinguished name enables you to unambiguously identify a specific target object. The distinguished name consists of a series of relative names:
dn = {rn}/{rn}/{rn}/{rn}...
In this example, the DN provides a fully qualified path for the Atlanta Tenant
object. The DN specifies the exact managed object on which the API call is operating.
< dn =”uni/” />

## Slide 54
Mapping Documents to the Schema
Notes: The distinguished name enables you to unambiguously identify a specific target object. The distinguished name consists of a series of relative names:
dn = {rn}/{rn}/{rn}/{rn}...
In this example, the DN provides a fully qualified path for the Atlanta Tenant
object. The DN specifies the exact managed object on which the API call is operating.
< dn =”uni/” />

## Slide 55: Application Programmable Interface
Lesson 4
Modifying the Schema

## Slide 56
User prompt> curl -d <aaaUser name='admin' pwd='NXos12345'/> http://192.168.10.1/api/mo/aaaLogin.xml
Using CURL
<?xml version="1.0" encoding="UTF-8"?><imdata totalCount="1">
<aaaLogin token="wYUAAAAAAAAAAAAAAAAAAIv0B6YakgNwu9wkr/5kcQqIbb+1NxWGJKQ5ZmtC
9BcxSWVQ7x6DVAIkbygU/FN3pwU3yxJej5EZIYcPqlQxKqcT6WoNQkhcGaml2qZRmLPXTZazAFH4N
xMz0eaHLd/qaId01p4tQ6SvM/lXvCcS7vtbGisok2eQFM6hIVe+BjQDZektvU5XRR09vja4a74aXQ==
" siteFingerprint="OEDUutd5zUe2qPOj" refreshTimeoutSeconds="600" maximumLifetimeSeconds="86400"
guiIdleTimeoutSeconds="1200" restTimeoutSeconds="90" creationTime="1517167933"
firstLoginTime="1517167933" userName="admin" remoteUser="false" unixUserId="15374"
sessionId="xDHZXWTTTvC0R6aOhW9gDA==" lastName="" firstName="" changePassword="no"
version="3.1(1i)" buildTime="Wed Dec 20 21:18:06 PST 2017" node="topology/pod-1/node-1">
<aaaUserDomain name="all" rolesR="admin" rolesW="admin"><aaaReadRoles/><aaaWriteRoles>
<role name="admin"/></aaaWriteRoles></aaaUserDomain><DnDomainMapEntry dn="uni/tn-mgmt"
readPrivileges="admin" writePrivileges="admin"/><DnDomainMapEntry dn="uni/tn-infra"
readPrivileges="admin" writePrivileges="admin"/><DnDomainMapEntry dn="uni/tn-common"
readPrivileges="admin" writePrivileges="admin"/>
Input
Output
Notes: Command Line URL or cURL is a simple example to show how individual changes could be made using the XML-Schema. As you can see, the Input is the same XML document posted with the tags side by side. The url that is stating where to institute the XML document is at the end of the command. The input requires one of the 3 changes to be made to the redundancy.
The output XML-Schema document will echo all of the parameters if no filters are applied and will show the redundancy as being modified to “grid”.
cURL was inefficient at making independent changes which led to applications being made that would be able to clarify this action and keep it manageable and scalable.

## Slide 57
User prompt> curl --cookie APIC-Cookie="6oUAAAAAAAAAAAAAAAAAAIKJC0ooPuTmqR9xuFUvDGV2FPxLF8DEEgNQl8+hsT2MZ00TABS7TR8eQoJwtGoogXb+zFAgNlQiBXEiK8oenmM9Wrclp8U2rfXEAN2C6MIU7X4ew1pYG6pp4zs4hEwu8lpQCKX8X3Gm7KS6TribjpH/P0CV+BtooDSs5VAilYRubkLaDddidEGxpnl0B91+Ig==" -d '<?xml version="1.0" encoding="UTF-8"?><fvTenant descr="" dn="uni/tn-PROD_SDN2" name="PROD_SDN2" nameAlias="" ownerKey="" ownerTag=""/>' http://192.168.10.1/api/mo/uni/tn-PROD_SDN2.xml
Using CURL
<?xml version="1.0" encoding="UTF-8"?><imdata totalCount="0"></imdata>
Input
Output
Notes: Command Line URL or cURL is a simple example to show how individual changes could be made using the XML-Schema. As you can see, the Input is the same XML document posted with the tags side by side. The url that is stating where to institute the XML document is at the end of the command. The input requires one of the 3 changes to be made to the redundancy.
The output XML-Schema document will echo all of the parameters if no filters are applied and will show the redundancy as being modified to “grid”.
cURL was inefficient at making independent changes which led to applications being made that would be able to clarify this action and keep it manageable and scalable.

## Slide 58
from ucsmsdk.ucshandle import UcsHandle
from ucsmsdk.mometa.compute.ComputePsuPolicy import ComputePsuPolicy
# Create a connection handle
handle = UcsHandle("172.16.48.135", "cisco", "cisco")
# Login to the server
handle.login()
# Login to the server
powerpol = ComputePsuPolicy(parent_mo_or_dn= "org-root", redundancy = 'grid' )
handle.add_mo(powerpol, modify_present = True)
#commit the configuration and logout
handle.commit()
handle.logout()
<xs:attribute name="redundancy">
<xs:annotation>
<xs:appinfo>
<moProperty value="computePsuDef:redundancy"/>
<label value="Redundancy" default="true"/>
<externAccess value="readWrite"/>
<description value="NO COMMENTS"/>
</xs:appinfo>
</xs:annotation>
<xs:simpleType>
<xs:restriction base="xs:string">
<xs:enumeration value="non-redundant"/>
<xs:enumeration value="n+1"/>
<xs:enumeration value="grid"/>
</xs:restriction>
</xs:simpleType>
</xs:attribute>
Using Python with an API
Notes: Many vendors are beginning to create a native Python API that can interact with the schema on the appliance. This allows the user to leverage the power of automation by repeating actions over and over as well as taking advantage of an Object Oriented programming approach to manage the flow of the script easier.

## Slide 59
from ucsmsdk.ucshandle import UcsHandle
from ucsmsdk.mometa.compute.ComputePsuPolicy import ComputePsuPolicy
# Create a connection handle
handle = UcsHandle("172.16.48.135", "cisco", "cisco")
# Login to the server
handle.login()
# Login to the server
powerpol = ComputePsuPolicy(parent_mo_or_dn= "org-root", redundancy = 'grid' )
handle.add_mo(powerpol, modify_present = True)
#commit the configuration and logout
handle.commit()
handle.logout()
<xs:attribute name="redundancy">
<xs:annotation>
<xs:appinfo>
<moProperty value="computePsuDef:redundancy"/>
<label value="Redundancy" default="true"/>
<externAccess value="readWrite"/>
<description value="NO COMMENTS"/>
</xs:appinfo>
</xs:annotation>
<xs:simpleType>
<xs:restriction base="xs:string">
<xs:enumeration value="non-redundant"/>
<xs:enumeration value="n+1"/>
<xs:enumeration value="grid"/>
</xs:restriction>
</xs:simpleType>
</xs:attribute>
Using Python with an API

## Slide 60
from ucsmsdk.ucshandle import UcsHandle
from ucsmsdk.mometa.compute.ComputePsuPolicy import ComputePsuPolicy
# Create a connection handle
handle = UcsHandle("172.16.48.135", "cisco", "cisco")
# Login to the server
handle.login()
# Login to the server
powerpol = ComputePsuPolicy(parent_mo_or_dn= "org-root", redundancy = 'grid' )
handle.add_mo(powerpol, modify_present = True)
#commit the configuration and logout
handle.commit()
handle.logout()
<xs:attribute name="redundancy">
<xs:annotation>
<xs:appinfo>
<moProperty value="computePsuDef:redundancy"/>
<label value="Redundancy" default="true"/>
<externAccess value="readWrite"/>
<description value="NO COMMENTS"/>
</xs:appinfo>
</xs:annotation>
<xs:simpleType>
<xs:restriction base="xs:string">
<xs:enumeration value="non-redundant"/>
<xs:enumeration value="n+1"/>
<xs:enumeration value="grid"/>
</xs:restriction>
</xs:simpleType>
</xs:attribute>
Using Python with an API

## Slide 61
from ucsmsdk.ucshandle import UcsHandle
from ucsmsdk.mometa.compute.ComputePsuPolicy import ComputePsuPolicy
# Create a connection handle
handle = UcsHandle("172.16.48.135", "cisco", "cisco")
# Login to the server
handle.login()
# Login to the server
powerpol = ComputePsuPolicy(parent_mo_or_dn= "org-root", redundancy = 'grid' )
handle.add_mo(powerpol, modify_present = True)
#commit the configuration and logout
handle.commit()
handle.logout()
<xs:attribute name="redundancy">
<xs:annotation>
<xs:appinfo>
<moProperty value="computePsuDef:redundancy"/>
<label value="Redundancy" default="true"/>
<externAccess value="readWrite"/>
<description value="NO COMMENTS"/>
</xs:appinfo>
</xs:annotation>
<xs:simpleType>
<xs:restriction base="xs:string">
<xs:enumeration value="non-redundant"/>
<xs:enumeration value="n+1"/>
<xs:enumeration value="grid"/>
</xs:restriction>
</xs:simpleType>
</xs:attribute>
Using Python with an API

## Slide 62
from ucsmsdk.ucshandle import UcsHandle
from ucsmsdk.mometa.compute.ComputePsuPolicy import ComputePsuPolicy
# Create a connection handle
handle = UcsHandle("172.16.48.135", "cisco", "cisco")
# Login to the server
handle.login()
# Login to the server
powerpol = ComputePsuPolicy(parent_mo_or_dn= ”org-root", redundancy = 'grid' )
handle.add_mo(powerpol, modify_present = True)
#commit the configuration and logout
handle.commit()
handle.logout()
<xs:attribute name="redundancy">
<xs:annotation>
<xs:appinfo>
<moProperty value="computePsuDef:redundancy"/>
<label value="Redundancy" default="true"/>
<externAccess value="readWrite"/>
<description value="NO COMMENTS"/>
</xs:appinfo>
</xs:annotation>
<xs:simpleType>
<xs:restriction base="xs:string">
<xs:enumeration value="non-redundant"/>
<xs:enumeration value="n+1"/>
<xs:enumeration value="grid"/>
</xs:restriction>
</xs:simpleType>
</xs:attribute>
Using Python with an API

## Slide 63
import requests
url = http://172.16.48.135/nuova/
headers = {
'content-type': "application/xml",
'cache-control': "no-cache"
}
data = '<configConfMos inHierarchical="no"><inConfigs><pair\
key="org-root/psu-policy"><computePsuPolicy descr=""\
dn="org-root/psu-policy"policyOwner="local” redundancy="grid"></computePsuPolicy>\
</pair></inConfigs></configConfMos>’
response = requests.post(url, headers=headers, data = data)
<xs:attribute name="redundancy">
<xs:annotation>
<xs:appinfo>
<moProperty value="computePsuDef:redundancy"/>
<label value="Redundancy" default="true"/>
<externAccess value="readWrite"/>
<description value="NO COMMENTS"/>
</xs:appinfo>
</xs:annotation>
<xs:simpleType>
<xs:restriction base="xs:string">
<xs:enumeration value="non-redundant"/>
<xs:enumeration value="n+1"/>
<xs:enumeration value="grid"/>
</xs:restriction>
</xs:simpleType>
</xs:attribute>
PYTHON without the native API
Notes: Since most vendors are still writing the Python API and updating their documentation, there is another way to interface with the RESTful interface by wrapping it with Python. This is accomplished through the “requests” module. It also useful to import like JSON and Beautiful Soup to help parse the objects. This will be a good method during the transitional phase while vendors get everything in order.

## Slide 64: Application Programmable Interface
Lesson 5
Data Maniputation and Extraction

## Slide 65
Loading JSON
import simplejson as json
file = "/home/student/parse_json.json"
test = open(file, 'r')
readfile = test.read()
data = json.loads(readfile)
test.close()
print data
{'TOP_OBJ': {'attributes': {'ownerKey': u'', 'name': 'TEST1_OBJECT',
'descr': 'This is a main section', 'ownerTag': u''}, 'children': [{'OBJ1': {'attributes':
{'ownerKey': u'', 'name': 'TEST2_OBJECT', 'descr': 'This is a second section', 'ownerTag': u''}}},
{'OBJ2': {'attributes': {'ownerKey': u'', 'name': 'TEST2_OBJECT',
'descr': 'This is a second section', 'ownerTag': u''}, 'children': [{'SUB_OBJ2':
{'attributes': {'prio': '1', 'type': 'String', 'name': 'TEST3_OBJECT', 'descr': 'This is third section'}}}]}}]}}
Notes: Data extraction is an important facet to why things are changing so quickly. No longer is a network looked at as being a means of just piping traffic from one point to another. It is also a represents a central location where data can be extracted to help Data Scientist forecast financial objectives and future use of company assets. JSON is becoming more and more popular as a way to represent the data with a key/value pair.

## Slide 66
Parsing JSON (Keys)
{
"TOP_OBJ": {
"attributes": {
"descr": "This is a main section",
"name": "TEST1_OBJECT",
"ownerKey": "",
"ownerTag": ""
},
"children": [{
"OBJ1": {
"attributes": {
"descr": "This is a second section",
"name": "TEST2_OBJECT",
"ownerKey": "",
"ownerTag": ""
}
}
}, {
"OBJ2": {
"attributes": {
"descr": "This is a second section",
"name": "TEST2_OBJECT",
"ownerKey": "",
"ownerTag": ""
},
"children": [{
"SUB_OBJ2": {
"attributes": {
"descr": "This is third section",
"type": "String",
"name": "TEST3_OBJECT",
"prio": "1"
}
}
}]
}
}]
}
}
import simplejson as json
file = "/home/student/parse_json.json"
test = open(file, 'r')
readfile = test.read()
data = json.loads(readfile)
test.close()
data1 = data["TOP_OBJ"]["attributes"]
print data1["name"]
Notes: In this example, a user is trying to extract the the name of the ‘TOP_OBJ’ located under the attributes section of that object. Regular expressions was the method used by parsing a string of text. With JSON, the text is organized like a Python dictionary that is nested by using dictionaries as values of other keys. This allows the user to call out an individual parameter without using special characters as with regular expressions.

## Slide 67
Parsing JSON (Keys)
{
"TOP_OBJ": {
"attributes": {
"descr": "This is a main section",
"name": "TEST1_OBJECT",
"ownerKey": "",
"ownerTag": ""
},
"children": [{
"OBJ1": {
"attributes": {
"descr": "This is a second section",
"name": "TEST2_OBJECT",
"ownerKey": "",
"ownerTag": ""
}
}
}, {
"OBJ2": {
"attributes": {
"descr": "This is a second section",
"name": "TEST2_OBJECT",
"ownerKey": "",
"ownerTag": ""
},
"children": [{
"SUB_OBJ2": {
"attributes": {
"descr": "This is third section",
"type": "String",
"name": "TEST3_OBJECT",
"prio": "1"
}
}
}]
}
}]
}
}
import simplejson as json
file = "/home/student/parse_json.json"
test = open(file, 'r')
readfile = test.read()
data = json.loads(readfile)
test.close()
data1 = data["TOP_OBJ"]["attributes"]
print data1["name"]

## Slide 68
Parsing JSON (Keys)
{
"TOP_OBJ": {
"attributes": {
"descr": "This is a main section",
"name": "TEST1_OBJECT",
"ownerKey": "",
"ownerTag": ""
},
"children": [{
"OBJ1": {
"attributes": {
"descr": "This is a second section",
"name": "TEST2_OBJECT",
"ownerKey": "",
"ownerTag": ""
}
}
}, {
"OBJ2": {
"attributes": {
"descr": "This is a second section",
"name": "TEST2_OBJECT",
"ownerKey": "",
"ownerTag": ""
},
"children": [{
"SUB_OBJ2": {
"attributes": {
"descr": "This is third section",
"type": "String",
"name": "TEST3_OBJECT",
"prio": "1"
}
}
}]
}
}]
}
}
import simplejson as json
file = "/home/student/parse_json.json"
test = open(file, 'r')
readfile = test.read()
data = json.loads(readfile)
test.close()
data1 = data["TOP_OBJ"]["attributes"]
print data1["name"]

## Slide 69
Parsing JSON (Keys)
{
"TOP_OBJ": {
"attributes": {
"descr": "This is a main section",
"name": "TEST1_OBJECT",
"ownerKey": "",
"ownerTag": ""
},
"children": [{
"OBJ1": {
"attributes": {
"descr": "This is a second section",
"name": "TEST2_OBJECT",
"ownerKey": "",
"ownerTag": ""
}
}
}, {
"OBJ2": {
"attributes": {
"descr": "This is a second section",
"name": "TEST2_OBJECT",
"ownerKey": "",
"ownerTag": ""
},
"children": [{
"SUB_OBJ2": {
"attributes": {
"descr": "This is third section",
"type": "String",
"name": "TEST3_OBJECT",
"prio": "1"
}
}
}]
}
}]
}
}
import simplejson as json
file = "/home/student/parse_json.json"
test = open(file, 'r')
readfile = test.read()
data = json.loads(readfile)
test.close()
data1 = data["TOP_OBJ"]["attributes"]
print data1["name"]

## Slide 70
Parsing JSON (Keys)
{
"TOP_OBJ": {
"attributes": {
"descr": "This is a main section",
"name": "TEST1_OBJECT",
"ownerKey": "",
"ownerTag": ""
},
"children": [{
"OBJ1": {
"attributes": {
"descr": "This is a second section",
"name": "TEST2_OBJECT",
"ownerKey": "",
"ownerTag": ""
}
}
}, {
"OBJ2": {
"attributes": {
"descr": "This is a second section",
"name": "TEST2_OBJECT",
"ownerKey": "",
"ownerTag": ""
},
"children": [{
"SUB_OBJ2": {
"attributes": {
"descr": "This is third section",
"type": "String",
"name": "TEST3_OBJECT",
"prio": "1"
}
}
}]
}
}]
}
}
import simplejson as json
file = "/home/student/parse_json.json"
test = open(file, 'r')
readfile = test.read()
data = json.loads(readfile)
test.close()
data1 = data["TOP_OBJ"]["attributes"]
print data1["name"]

## Slide 71
Parsing JSON (Keys)
{
"TOP_OBJ": {
"attributes": {
"descr": "This is a main section",
"name": "TEST1_OBJECT",
"ownerKey": "",
"ownerTag": ""
},
"children": [{
"OBJ1": {
"attributes": {
"descr": "This is a second section",
"name": "TEST2_OBJECT",
"ownerKey": "",
"ownerTag": ""
}
}
}, {
"OBJ2": {
"attributes": {
"descr": "This is a second section",
"name": "TEST2_OBJECT",
"ownerKey": "",
"ownerTag": ""
},
"children": [{
"SUB_OBJ2": {
"attributes": {
"descr": "This is third section",
"type": "String",
"name": "TEST3_OBJECT",
"prio": "1"
}
}
}]
}
}]
}
}
import simplejson as json
file = "/home/student/parse_json.json"
test = open(file, 'r')
readfile = test.read()
data = json.loads(readfile)
test.close()
data1 = data["TOP_OBJ"]["attributes"]
print data1["name"]

## Slide 72
Parsing JSON (Keys)
{
"TOP_OBJ": {
"attributes": {
"descr": "This is a main section",
"name": "TEST1_OBJECT",
"ownerKey": "",
"ownerTag": ""
},
"children": [{
"OBJ1": {
"attributes": {
"descr": "This is a second section",
"name": "TEST2_OBJECT",
"ownerKey": "",
"ownerTag": ""
}
}
}, {
"OBJ2": {
"attributes": {
"descr": "This is a second section",
"name": "TEST2_OBJECT",
"ownerKey": "",
"ownerTag": ""
},
"children": [{
"SUB_OBJ2": {
"attributes": {
"descr": "This is third section",
"type": "String",
"name": "TEST3_OBJECT",
"prio": "1"
}
}
}]
}
}]
}
}
import simplejson as json
file = "/home/student/parse_json.json"
test = open(file, 'r')
readfile = test.read()
data = json.loads(readfile)
test.close()
data1 = data["TOP_OBJ"]["attributes"]
print data1["name"]

## Slide 73
Parsing JSON(Lists)
{
"TOP_OBJ": {
"attributes": {
"descr": "This is a main section",
"name": "TEST1_OBJECT",
"ownerKey": "",
"ownerTag": ""
},
"children": [{
"OBJ1": {
"attributes": {
"descr": "This is a second section",
"name": "TEST2_OBJECT",
"ownerKey": "",
"ownerTag": ""
}
}
}, {
"OBJ2": {
"attributes": {
"descr": "This is a second section",
"name": "TEST2_OBJECT",
"ownerKey": "",
"ownerTag": ""
},
"children": [{
"SUB_OBJ2": {
"attributes": {
"descr": "This is third section",
"type": "String",
"name": "TEST3_OBJECT",
"prio": "1"
}
}
}]
}
}]
}
}
import simplejson as json
file = "/home/student/parse_json.json"
test = open(file, 'r')
readfile = test.read()
data = json.loads(readfile)
test.close()
data1 = data["TOP_OBJ"]["children"]
print data1[0]
print data1[1]
Notes: In some cases, the nested dictionaries are broken up into a list of dictionaries. This helps to relax the naming space and allows the same types of keys to be reused. This is a powerful way to store the data to be extracted and looped through. It also allows the user to grab a specific value of interest that may be stored under a number of different objects.
The difference in parsing this about is paying attention to when the list begins as they are referenced by an index and not a key. The example shows how OBJ1 and OBJ2 must first be referenced by the index placement of “0” and “1” respectively before calling out the key value. The nested dictionary approach can continue once this has been accomplished.

## Slide 74
Parsing JSON (Keys)
{
"TOP_OBJ": {
"attributes": {
"descr": "This is a main section",
"name": "TEST1_OBJECT",
"ownerKey": "",
"ownerTag": ""
},
"children": [{
"OBJ1": {
"attributes": {
"descr": "This is a second section",
"name": "TEST2_OBJECT",
"ownerKey": "",
"ownerTag": ""
}
}
}, {
"OBJ2": {
"attributes": {
"descr": "This is a second section",
"name": "TEST2_OBJECT",
"ownerKey": "",
"ownerTag": ""
},
"children": [{
"SUB_OBJ2": {
"attributes": {
"descr": "This is third section",
"type": "String",
"name": "TEST3_OBJECT",
"prio": "1"
}
}
}]
}
}]
}
}
import simplejson as json
file = "/home/student/parse_json.json"
test = open(file, 'r')
readfile = test.read()
data = json.loads(readfile)
test.close()
data1 = data["TOP_OBJ"]["chidren"]
print data1[0]
print data1[1]

## Slide 75
Parsing JSON (Keys)
{
"TOP_OBJ": {
"attributes": {
"descr": "This is a main section",
"name": "TEST1_OBJECT",
"ownerKey": "",
"ownerTag": ""
},
"children": [{
"OBJ1": {
"attributes": {
"descr": "This is a second section",
"name": "TEST2_OBJECT",
"ownerKey": "",
"ownerTag": ""
}
}
}, {
"OBJ2": {
"attributes": {
"descr": "This is a second section",
"name": "TEST2_OBJECT",
"ownerKey": "",
"ownerTag": ""
},
"children": [{
"SUB_OBJ2": {
"attributes": {
"descr": "This is third section",
"type": "String",
"name": "TEST3_OBJECT",
"prio": "1"
}
}
}]
}
}]
}
}
import simplejson as json
file = "/home/student/parse_json.json"
test = open(file, 'r')
readfile = test.read()
data = json.loads(readfile)
test.close()
data1 = data["TOP_OBJ"]["chidren"]
print data1[0]
print data1[1]

## Slide 76
Parsing JSON (Keys)
{
"TOP_OBJ": {
"attributes": {
"descr": "This is a main section",
"name": "TEST1_OBJECT",
"ownerKey": "",
"ownerTag": ""
},
"children": [{
"OBJ1": {
"attributes": {
"descr": "This is a second section",
"name": "TEST2_OBJECT",
"ownerKey": "",
"ownerTag": ""
}
}
}, {
"OBJ2": {
"attributes": {
"descr": "This is a second section",
"name": "TEST2_OBJECT",
"ownerKey": "",
"ownerTag": ""
},
"children": [{
"SUB_OBJ2": {
"attributes": {
"descr": "This is third section",
"type": "String",
"name": "TEST3_OBJECT",
"prio": "1"
}
}
}]
}
}]
}
}
import simplejson as json
file = "/home/student/parse_json.json"
test = open(file, 'r')
readfile = test.read()
data = json.loads(readfile)
test.close()
data1 = data["TOP_OBJ"]["chidren"]
print data1[0]
print data1[1]

## Slide 77
Parsing JSON (Keys)
{
"TOP_OBJ": {
"attributes": {
"descr": "This is a main section",
"name": "TEST1_OBJECT",
"ownerKey": "",
"ownerTag": ""
},
"children": [{
"OBJ1": {
"attributes": {
"descr": "This is a second section",
"name": "TEST2_OBJECT",
"ownerKey": "",
"ownerTag": ""
}
}
}, {
"OBJ2": {
"attributes": {
"descr": "This is a second section",
"name": "TEST2_OBJECT",
"ownerKey": "",
"ownerTag": ""
},
"children": [{
"SUB_OBJ2": {
"attributes": {
"descr": "This is third section",
"type": "String",
"name": "TEST3_OBJECT",
"prio": "1"
}
}
}]
}
}]
}
}
import simplejson as json
file = "/home/student/parse_json.json"
test = open(file, 'r')
readfile = test.read()
data = json.loads(readfile)
test.close()
data1 = data["TOP_OBJ"]["chidren"]
print data1[0]
print data1[1]
INDEX “0”

## Slide 78
Parsing JSON (Keys)
{
"TOP_OBJ": {
"attributes": {
"descr": "This is a main section",
"name": "TEST1_OBJECT",
"ownerKey": "",
"ownerTag": ""
},
"children": [{
"OBJ1": {
"attributes": {
"descr": "This is a second section",
"name": "TEST2_OBJECT",
"ownerKey": "",
"ownerTag": ""
}
}
}, {
"OBJ2": {
"attributes": {
"descr": "This is a second section",
"name": "TEST2_OBJECT",
"ownerKey": "",
"ownerTag": ""
},
"children": [{
"SUB_OBJ2": {
"attributes": {
"descr": "This is third section",
"type": "String",
"name": "TEST3_OBJECT",
"prio": "1"
}
}
}]
}
}]
}
}
import simplejson as json
file = "/home/student/parse_json.json"
test = open(file, 'r')
readfile = test.read()
data = json.loads(readfile)
test.close()
data1 = data["TOP_OBJ"]["chidren"]
print data1[0]
print data1[1]
INDEX “1”